## Slide 1: BITS Pilani Digital Design
Prof. GSS Chalapathi, Prof. Saurabh Gandhi (EEE department)

## Slide 2
Review questions

## Slide 3
Programmable logic devices
Fixed logic circuit
Simple programmable logic device built using antifuses that can be burned in
What would happen without the pull-up resistors on each input?

## Slide 4
Programmable logic devices

## Slide 5
Memory in which permanent binary information / combinational circuit is stored
Remember: “decoders are minterm generators”
Also “any combinational logic can be represented as sum of minterms”
ROM includes decoders and OR gates within a single IC  decoder outputs may be sent to several OR gates
Connections between decoder outputs and OR gates is ‘programmable’ to implement different functions
Read Only Memory (ROM)
The circuit below will allow you to generate

## Slide 6
Implement: V0 = m( 4, 6, 7); V1 = m( 2, 6, 7); V2 = m( 1,2,3,4)
Implementing a Boolean function with a ROM

## Slide 7
New symbols

## Slide 8
Circuit is performing a computation on inputs A2A1A0 to produce output V2V1V0
The same input will generate the same output every time
Circuit “remembers” the output for each possible input
How many values of what bit width does this circuit ‘remember’?
A2A1A0 forms an address that refers to one of the 8 stored values
Read Only because once the OR gate inputs are fused, they cannot be changed.
Why do we call this a ‘memory’?

## Slide 9
Example: output is square of input
ROM implementation is not efficient for inputs with many don’t care condition
What sized ROM would you need to implement the truth table shown?
Notes: What does don’t care mean in terms of output OR gate connections in a ROM?

## Slide 10
A ROM uses a decoder to generate all possible minterms, with no circuit minimization
ROM implementation of an n-input function uses many gates:
  n-to-2n decoder (which has n inverters and 2n n-input AND gates)
  OR gate with 2n inputs
  Number of gates roughly doubles for each additional ROM input
A PLA makes the decoder part of the ROM also programmable
You can choose what products (not necessarily minterms) to generate
Programmable Logic Arrays (PLAs)

## Slide 11
A 3 x 4 x 3 PLA

## Slide 12
Optimizing expressions for PLA implementation
What size PLA would be required to implement these functions?

## Slide 13
Optimizing expressions for PLA implementation
What size PLA would be required to implement these functions?

## Slide 14
Implementing our example with PLA

## Slide 15
Implement the two functions given below using a 3x4x2 PLA:
F1=(0,1,2,4)
F2= (0,5,6,7)
Example 2

## Slide 16
Example 2 – circuit implementation

## Slide 17
PLA summary

## Slide 18
Programmable logic devices

## Slide 19
OR array is fixed, AND array can be programmed
Less flexible than PLA
Number of product terms available per function is fixed
Programmable Array Logic (PAL)
Only functions with at most four products can be implemented

## Slide 20
W = ABC + CD
X = ABC + ACD + ACD + BCD
Y = ACD + ACD + ABD
Example

## Slide 21
What if you allowed outputs to be connected back as inputs?
More complex functions using PALs

## Slide 22
Implement the following equations using a PAL with 4 inputs, 4 outputs, and 3-wide AND-OR structure.
  W(A, B, C, D) = m(2, 12, 13)
  X(A, B, C, D) = m(7, 8, 9, 10, 11, 12, 13, 14, 15)
  Y(A, B, C, D) = m(0, 2, 3, 4, 5, 6, 7, 8, 10, 11, 15)
  Z(A, B, C, D) = m(1, 2, 8, 12, 13)
Simplification:
  W = ABC’ + A’B’CD’
  X = A + BCD
  Y = A’B + CD + B’D’
  Z = ABC’ + A’B’CD’ + AC’D’ + A’B’C’D
    = W + AC’D’+A’B’C’D
Example 2

## Slide 23
Example 2 – tabular specification

## Slide 24
F1 (a, b, c) =  (6, 7)
F2 (a, b, c) =  (4, 5, 7)
F3 (a, b, c) =  (3, 5)
F4 (a, b, c) =  (2, 6)
Implement using PLA