## Slide 1: BITS Pilani Digital Design
Prof. GSS Chalapathi, Prof. Saurabh Gandhi (EEE department)

## Slide 2
A counter is a register that goes through a predetermined sequence of states upon the application of clock pulses.
Categorized as:
  Ripple counters The FF output transition serves as a source for triggering other FFs. NO COMMON CLOCK.
  Synchronous counters All FFs receive the common clock pulse, and the change of state is determined based on the present state
Counters

## Slide 3
Less significant bit serves as the clock for the next significant bit (negative edge clock)
4-bit binary up counter

## Slide 4
The output of each FF is connected to the C input of the next FF in sequence.
The FF holding the least significant bit receives the incoming clock pulses.
The J and K inputs of all FFs are connected to a permanent logic 1.
The bubble next to the C label indicates that the FFs respond to the negative-going transition of the input.
4-bit binary up counter

## Slide 5
4-bit binary up counter

## Slide 6
4-bit ripple counters (other designs)

## Slide 7
Use direct set (S) instead of direct reset (R) to start at 1111 instead of 0000
Design the rest on your own…
4-bit binary down counter

## Slide 8
BCD ripple counter
Q1 complemented on every clock edge
Q2 complemented if Q8 = 0, Q1 goes from 1 to 0.
Q2 cleared if Q8 = 1 and Q1 goes from 1 to 0
Q4 complemented when Q2 goes from 1 to 0
Q8 complemented when Q4Q2 = 11, Q1 goes from 1 to 0.
Q8 cleared if either Q4 or Q2 is 0 and Q1 goes from 1 to 0

## Slide 9
The ‘ripple’ in BCD ripple counters

## Slide 10
Same design procedure as other sequential circuits
Inputs: clock and control signals (EN, Load etc)
Outputs: FF states
Most efficient implementations use T or JK FFs
Synchronous binary counters

## Slide 11
JK synchronous binary counter

## Slide 12
JK synchronous binary counter

## Slide 13
JK synchronous binary counter

## Slide 14
JK synchronous binary counter

## Slide 15
JK synchronous binary counter

## Slide 16
JK synchronous binary counter with EN and CO
EN = enable control signal, when 0 counter remains in the same state, when 1 it counts
JQ0 = 1 · EN
KQ0 = 1 · EN
JQ1 = Q0 · EN
KQ1 = Q0 · EN
JQ2 = Q0 Q1 · EN
KQ2 = Q0 Q1 · EN
JQ3 = Q0 Q1 Q2 · EN
KQ3 = Q0 Q1 Q2 · EN
C0 = Q0 Q1 Q2 Q3 · EN
CO = carry output signal:
used to extend the counter to more stages
…how?

## Slide 17
If serial gating (chain of gates, info ripples through) is used  serial counter
If serial gating is replaced with parallel gating (this is analogous with ripple-logic replaced with carry-lookeahead logic in our adder designs)  parallel counter
Advantage of parallel over serial counter: faster in certain occasions (1111  0000)
Serial vs parallel counters

## Slide 18
Up – Down binary counters

## Slide 19
Up – Down binary counters
1 0 0 0 1 1 1
1 0 0 1 0 0 0
1 0 1 0 0 0 1
1 0 1 1 0 1 0
1 1 0 0 0 1 1
1 1 0 1 1 0 0
1 1 1 0 1 0 1
1 1 1 1 1 1 0
UD Q2 Q1 Q0 Q2.D Q1.D Q0.D
0 0 0 0 0 0 1
0 0 0 1 0 1 0
0 0 1 0 0 1 1
0 0 1 1 1 0 0
0 1 0 0 1 0 1
0 1 0 1 1 1 0
0 1 1 0 1 1 1
0 1 1 1 0 0 0
UD Q2 Q1 Q0 Q2.D Q1.D Q0.D
Up-Counter
Down-Counter

## Slide 20
Up – Down binary counters

## Slide 21
Up – Down binary counters

## Slide 22
Ability to set the counter to an arbitrary value to begin counting
Binary counter with parallel load
Load | Count | Operation
0 | 0 | Nothing
0 | 1 | Count
1 | x | Load

## Slide 23
BCD counter using parallel load counter
The counter starts with an all-zero output.
As long as the output of the AND gate is 0, each positive clock pulse transition increments the counter by one.
When the output reaches the count of 1001, both Q0 and Q3 become 1, making the output of the AND gate equal to 1. This condition makes Load active, so on the next clock transition, the counter does not count, but is loaded from its four inputs.
The value loaded then is 0000.

## Slide 24
Given an arbitrary sequence, design a counter that will generate the sequence
Procedure:
  Derive state table / diagram based on the sequence
  Simplify
  Build the circuit
Example: Use D-FFs to design a sequence generator for the sequence: 0  7  6  1  0 (000  111  110  001  000)
Arbitrary sequence counter

## Slide 25
Counters with unused states

## Slide 26
Ring counter

## Slide 27
Johnson counter